## Slide 1
DIGITAL DESIGN & COMPUTER ARCHITECTURE
8-BIT SIPO
SHIFT REGISTER
Serial-In, Parallel-Out
Design • Working • Applications
1
0
1
1
0
0
1
0
A simple way to receive, store and output 8 bits of data.
DDCA | Sequential logic

## Slide 2
01 • CORE CONCEPT
What does SIPO mean?
One bit enters at a time; eight stored bits are available at separate outputs.
02 / 06
S
SERIAL-IN
Data enters one bit at a time through a single input line.
I
SHIFT
Each clock edge moves stored data to the next flip-flop.
P
PARALLEL-OUT
The outputs Q0–Q7 show the stored bits together.
THE DESIGN
8 D flip-flops + 1 shared clock + 1 serial input = 8-bit SIPO register
Each D flip-flop stores one bit. Eight flip-flops therefore store eight bits.

## Slide 3
02 • CIRCUIT DESIGN
8-bit SIPO circuit
Connect each Q output to the next D input. All flip-flops share the same clock.
03 / 06
SERIAL IN
FF0
D Q
Q0
FF1
D Q
Q1
FF2
D Q
Q2
FF3
D Q
Q3
FF4
D Q
Q4
FF5
D Q
Q5
FF6
D Q
Q6
FF7
D Q
Q7
COMMON CLOCK
Parallel outputs: Q0, Q1, Q2, Q3, Q4, Q5, Q6, Q7
PASTE YOUR LOGISIM SCREENSHOT HERE
Replace this placeholder with your circuit simulation image.
DESIGN CHECKLIST
8 D flip-flops
Shared clock
Q → next D
8 outputs
Tip: label SI, CLK and Q0–Q7 in Logisim.

## Slide 4
03 • WORKING EXAMPLE
How the bits shift
Example input sequence: 1 → 0 → 1 → 1 → 0 → 0 → 1 → 0
04 / 06
CLOCK PULSE
SERIAL INPUT
REGISTER (FF7 → FF0)
Initial
—
00000000
1
1
00000001
2
0
00000010
3
1
00000101
4
1
00001011
5
0
00010110
6
0
00101100
7
1
01011001
8
0
10110010
WHAT TO NOTICE
Each rising clock edge shifts the data one stage.
The newest bit enters FF0.
After 8 pulses, all 8 input bits are stored.
Final register: 10110010
(read FF7 → FF0)

## Slide 5
04 • APPLICATIONS
Where is a SIPO register used?
It is useful whenever serial data needs to become multiple digital outputs.
05 / 06
01
LED control
Control several LEDs while using fewer microcontroller output pins.
02
Serial-to-parallel conversion
Collect incoming serial bits and present them together at separate outputs.
03
Display interfaces
Drive indicator panels and support digital display/control circuits.
Real-world example: the 74HC595 is a common shift-register IC used to expand digital outputs.

## Slide 6
05 • WRAP-UP
Conclusion
One circuit, one bit at a time, eight outputs together.
06 / 06
REMEMBER THESE 4 POINTS
SIPO = Serial-In, Parallel-Out.
Eight D flip-flops store eight bits.
A shared clock controls the shifting.
Parallel outputs make all stored bits available together.
FINAL OUTPUT
10110010
After 8 clock pulses
for the example input sequence
THANK YOU
Questions?
Tip for presenting: point to the circuit, explain one clock pulse, then show the final output.